## Slide 1: KRSSG Reading Round
Transmission control protocol/Internet Protocol(TCP/IP)
Genetic Algorithms
Path Planning Algorithms

## Slide 2: TCP/IP
This is a internet protocol created for efficient data transmission.
The TCP takes care of division of data into multiple bytes of data, aggregation of data and checks if there are errors in the transmission.
The IP takes care of transmission of the packets(bytes) of data.
This is done by referencing each packet and also optimising the path using path planning algorithms.

## Slide 3: Mechanism
IP Packet Routing: The IP layer handles the routing of IP packets across networks. It uses algorithms such as the Shortest Path First (SPF) algorithm, commonly implemented as Open Shortest Path First (OSPF) or Routing Information Protocol (RIP), to determine the most efficient path for packet transmission. This algorithm uses Dijkstra’s algorithm to get the shortest path.
TCP Connection Establishment and Termination: The Transmission Control Protocol (TCP) is responsible for establishing, maintaining, and terminating reliable connections between devices. The three-way handshake is used for connection establishment, where a series of SYN (synchronize) and ACK (acknowledge) packets are exchanged between the client and server.
Packet Sequencing and Acknowledgment: TCP breaks data into smaller units called segments and assigns sequence numbers to ensure ordered delivery. The receiver acknowledges the receipt of segments by sending ACK packets, and the sender retransmits any unacknowledged segments.
Congestion Control: TCP employs various congestion control algorithms to manage network congestion and ensure efficient data transmission. Common algorithms include Slow Start, Congestion Avoidance, Fast Retransmit, and Fast Recovery. These algorithms dynamically adjust the transmission rate based on network conditions and received acknowledgments.

## Slide 4: Mechanism
Error Detection and Correction: TCP/IP uses error detection mechanisms, such as checksums, to ensure the integrity of transmitted data. The receiving end verifies the checksum to detect errors and requests retransmission if errors are detected.
Fragmentation and Reassembly: IP handles packet fragmentation and reassembly when data exceeds the maximum transmission unit (MTU) size of the network. It fragments large IP packets into smaller units and reassembles them at the destination.
Address Resolution: Address Resolution Protocol (ARP) resolves IP addresses to their corresponding MAC addresses in a local network. ARP broadcasts requests to obtain MAC addresses and caches the mapping for future use.

## Slide 5: Genetic Algorithm
These are the algorithms derived from the way nature improves on its own, the process of natural Selection.
It incorporates the ideas related to natural selection like individuals, breeding, mutation, etc to the problem to get an approximate result(generally).
This is done for problems that are very lengthy to compute exactly or those where an approximate solution is enough.
Here when we increase the number of interations, the result gets more accurate.

## Slide 6: Individuals
In this algorithm, we create random inputs initially to create the first generation and breed it to get a more accurate result.

## Slide 8: Individuals

## Slide 9: Path planning Algorithm:RRT
Rapidly exploring random tree is an algorithm which takes a random point and gets the node that is nearest to it and gets the path.